## Slide 1: Predicting Post-wildfire Soil Characteristics Using Remote Sensing and AI: A Case Study in Central Greece
Stylianos Manoudakis (Technical University of Crete)

## Slide 2: Description
Wildfires cause significant damage to ecosystems, particularly to soil health. Key challenges include:
Erosion: Soil becomes prone to displacement.
Nutrient Loss: Fires deplete essential nutrients like carbon and nitrogen.
Structural Issues: Soil compaction and pH imbalances hinder vegetation regrowth.
TREEADS Artificial intelligent Soil assessment, Agroforestry and Soil Enhancements and automation (Lead: TUC, Participants: SQD, UdG, GBD, LAMMC)
Utilize aerial means, remote sensing data to assess soil quality and evaluate physical, chemical indicators or characteristics of the soil such as pH and SoC. This information will enable the creation of a service that will propose agroforestry restoration techniques specific to the burned area.

## Slide 3: Methodology
Extraction of soil characteristics
Agroforestry Restoration Strategies
Integration to TREEADS Holistic platform
Prevention
& Preparedness
Detection
& Response
Restoration
& Adaptation
Notes: Semantic segmentation is a pixel and region of interest based approach
Approximation using pixel by pixel classification, in this study we implement pixel based regression
Practically, the network will learn to transform the image to features and then back to the same size prediction image, image we provided to the dataset

## Slide 4: Soil characteristics prediction
Sequoia sensor
Spectral band width:
Green: 530-570 nm
Red: 640-680 nm
Red Edge: 730-740 nm
Near Infrared: 770-810 nm
RGB Camera
Nikon D800
Four burned areas
Sampling & training datasets
2022: Itea-Delfoi (Burned area 4953.97 ha)
2023: Prodromos (Burned area 3466.89 ha)
Validation dataset
2022: Domokos (Burned area 309.05 ha)
2023: Yliki (Burned area 493.28 ha)

## Slide 5: Soil data sampling

## Slide 6: Soil data sampling

## Slide 7: Soil characteristics prediction
Machine Learning and DNN classification:
Random Forest
CART
Sequential Neural Networks
Figure 12. Visual representation of the Sequential neural network.
Notes: Semantic segmentation is a pixel and region of interest based approach
Approximation using pixel by pixel classification, in this study we implement pixel based regression
Practically, the network will learn to transform the image to features and then back to the same size prediction image, image we provided to the dataset

## Slide 8: Soil characteristics prediction
Prodromos texture class prediction
RF O.A 96,23%
Prodromos texture class prediction
CART OA 77,35%
Soil Characteristics Predictions for Prodromos burned area
Notes: Overfeed when the error is stable and not changing, the output of the network will be a georeferenced satellite image /w 15+6 bands Bands

## Slide 9: Agroforestry restoration DSS module
Vulnerability assessment
Set Data requirements
Trigger parameter
Restoration goal
Propose actions

## Slide 10: Agroforestry restoration module
Fire severity, classified values based on literature thresholds
T6.1 demonstration UI, classified assessment layers and the resulting restoration suggestion per intervention area

## Slide 11: TREEADS Soil restoration service

## Slide 12: TREEADS Artificial intelligent Soil assessment, Agroforestry and Soil Enhancements and automation
Utility tool for restoration stakeholders and actors
Rapid assessments
Scalable & case specific solutions
Sophisticated agroforestry restoration decision support system

## Slide 13
Thank you!
www.treeads-project.eu
@treeads-h2020
@TreeadsH2020
Do you have any questions?