## Slide 1: Webinar #6 - From Risk Scenarios to Response Plans with TREEADS Simulation Technologies
Workshop – 15 May 2025
Mabel Asensio-Sevilla
mas@usal.es
Diego González-Aguilera daguilera@usal.es
WebGIS-Integrated Wind–Fire–Smoke Modeling Tool

## Slide 2: WebGIS-Integrated Wind–Fire–Smoke Modeling Tool
Lead: USAL
Participants: SINUMCC, TIDOP
Main Contribution:
Design & development of simulation models
Participants:
M.I. Asensio
J.M. Cascón
J.M. Iglesias
Main Contribution:
Integration into WebGIS platform
Participants:
D. González-Aguilera
D. Cifuentes
P. De Andrés
S. Lagüela

## Slide 3
COUPLED MODELS SCHEME
  Fire spread model
  Wind field model
  Air dispersion model
NEPTUNO-GDAL (core)
DEM
Fuel type
Fuel load
Wind
Temperature
Humidity
Wind field
Fuel moisture content
Burned area(ha)
Burning areas(ha)
Rate of spread
Fuel consumed
Heat release rate
Smoke concentration
INPUT
MODEL
OUTPUT
PARAMETERS
Friction coeff.
Model parameters
Fuel type parameters
Dispersion coefficients
Emission factor
Notes: We have continue to work on the simulation of some historical fires in the Spanish pilot area, specifically the San Juan de la Nava and Gavilanes fires, both of moderate size.
The main problem we are facing is the lack of precise information, we only have the start date, duration, final perimeter and position of the starting point.
But it is essential to have accurate mapping of the vegetation in the days prior to the date of the fire, and accurate wind data during the fire, both intensity and direction.

## Slide 4
Webgis architecture

## Slide 5
WEBGIS PLATFORM WORKFLOW
SIMULATION AREA
M-I Area selection
Bounding box
Geo-referenced
GEO DATA
DEM, Fuel load, fuel type
FIRE SOURCE
M-II Fire source position
One or more points
Geo-referenced
FIREWALLS
M-III Firewalls position
Polyline
W-III
Firewall width
BASIC DATA EVENT
W-I Metadata
Title/date/description
W-II Configuration
Time/Output/Accuracy
Activate smoke
Activate fire-spotting
METEO DATA
W-IV Meteo data
Temperature/Humidity
W-IV Constant wind data
Wind: intensity/direction
METEO DATA
M-V Punctual wind data
One or more points
Geo-referenced
W-V Punctual wind data
Wind intensity/direction
MODELS CONFIGURATION
W-VI PhyFire configuration
Model parameters
W-VII HDWind configuration
Model parameters
W-VIII PhyNX configuration
Model parameters
FUEL CONFIGURATION
W-IX Fuel type dependent parameters
Flame temp/Pyrol temp/Flame height/Comb half-life/Max fuel load/FMC/Heat Capacity/Heat of comb/Rugosity
Front-End: Configuration stage

## Slide 6
WEBGIS PLATFORM WORKFLOW
Front-End: Configuration stage
Several base layers
Specific cartographies

## Slide 7
WEBGIS PLATFORM WORKFLOW
Front-End: Configuration stage
Basic configuration
New simulation

## Slide 8
WEBGIS PLATFORM WORKFLOW
Front-End: Configuration stage
Wind point data : Activate HDWind
Uniform wind data

## Slide 9
WEBGIS PLATFORM WORKFLOW
Back-End: Neptuno-Gdal Core
PROCESS
Running simulation
Progress state
POST-PROCESS
Join database
Generate video
PRE-PROCESS
Preparing data
WORKSPACE GENERATION
NEPTUNO-GDAL CORE

## Slide 10
WEBGIS PLATFORM WORKFLOW
Front-End: Visualization stage
DISPLAY PHYFIRE RESULTS
S-I Burned area
S-I Burning area
S-I Statistics (ROS, ha…)
W-XII 3D animation
DISPLAY HDWIND RESULTS
S-I & II Wind field
DISPLAY PHYNX RESULTS
S-I & II Smoke concentration

## Slide 11: WebGIS-Integrated Wind–Fire–Smoke Modeling Tool
Lead: USAL
Participants: SINUMCC, TIDOP
THANK YOU FOR YOUR ATTENTION!
ARE THERE ANY QUESTIONS?
Mail to: mas@usal.es
M.I. Asensio